## Slide 1: CAESAR – GFA Piquet
Alain Bertrand :: Paul Scherrer Institut

## Slide 2: CAESAR main goals
What is it
How to access it
Live monitoring
Network overview
Log in / Permissions
Restarting / Upgrading a gateway
Checking Gateway software version
Debugging EPICS
Configuration
Log view / analyze

## Slide 3: What is it
CAESAR stands for:
CA EPICS Spy And Report
Goal:
1 pit stop point for all the EPICS Gateway work

## Slide 4: How to access it
https://caesar.psi.ch/

## Slide 5: Live monitoring
From the “Status” tab click on any gateway and a detailed view will be displayed

## Slide 6: Network overview
The map tab on top shows an overview of all the gateways.
Mouse over any and more information will be displayed.

## Slide 7: Log in / Permissions
All monitoring, checking, log analyze doesn’t require login.
Configuration change, restart a gateway do require a login.
Windows Username & Password used

## Slide 8: Restarting / Upgrading a gateway
In the status detail view, press “Restart” or “Upgrade”
A confirmation dialog will be displayed
Press “OK” and the gateway shall restart.

## Slide 9: Checking Gateway software version
Select “Gateway Versions” in the hamburger menu
You get a list of all Gateways with the version they are running.
Old versions will be displayed with red background
1

## Slide 10: Debugging EPICS
Select “EPICS Debug” in the hamburger menu
Type in a PV you want to check
Select a gateway you want to try on
Press run and wait…
Check out the result
1
2
3
4
5

## Slide 11: Configuration
From the detailed view click “Configuration”
And the gateway configuration will be displayed.
New configuration will be applied only after restarting the gateway.

## Slide 12: Log view / analyze
From the detailed view click “Logs”
And the gateway logs will be displayed.

## Slide 13: Log view / analyze
Stat bars (10 min bars):
Top => Number of log entries
Bottom => Number of searches
Red Line => Number of errors
Black Line => CPU load
Click on any bar to start looking for logs entries at that period

## Slide 14: Log view / analyze
From the log view, once a 10 min slot is selected click on the small “…” button
Select one of the pre-made query
And the report shall be displayed on the bottom part
1
2
3

## Slide 15: Wir schaffen Wissen – heute für morgen
Questions?
Contacts:
alain.bertrand@psi.ch